# Library Construction

Using another piece, mark width along front and back edges of sides F + G.

Pre-drill holes (4 for front, 3 for back) using 3/32” bit.

Position back A and one side F and pre-drill holes into side using 3/32” bit.  Install trim screws.  (3 total).  Position other side G and pre-drill holes.  Install trim screws.  (3 total)

Insert floor B supported by base K  ~2” above work surface.

Mark where top (and bottom) of floor meets sides, front and back.  Remove floor.

Pre-drill holes (2 for each side, 3 for front and back).  Re-insert floor.  Install trim screws.  (7 total)

Position front D and pre-drill holes.  Install trim screws. (11 total)

Squirt glue and install outside molding L + M (to cover trim screws).  Secure with ⅝” nails (4 on each side).  (32 total)

# Roof Construction

Squirt glue and position trim N + P (flush with top of roof) and secure with ⅝” nails (4 for each side, 5 for front and back)  (18 total)

# Door Construction

Squirt glue and install outside molding Q + R (for window) and secure with ⅝” nails (2 for each side, 3 for top and bottom)  (10 total)

# Painting

Paint all surfaces of library, roof and door.  Door and roof can be contrasting color.  Let dry for 48 hours.  Paint again with second coat.  Paint codes labels provided, but are also at Home Depot under 512-964-3890.

# Window Installation

Peel back protective film from all edges on both sides for about ½”.  Secure film with masking tape.

Squirt silicone along recess of door and position window.  Use finger to remove excess silicone

# Hinge Installation

Position hinges 3” from top and bottom of door C.  Pre-drill holes using 3/32” bit. Install screws.

Position slide bolt 3” from bottom of door.  Pre-drill holes using 3/32” bit.  Install screws.

Center door above library opening (with hinges folded underneath).  Carefully open door and mark positon of holes.  Pre-drill holes using 3/32” bit.  Install screws to secure door to library.

Position spacer under center of slide bolt.  Install with 1 drywall screw.

Position slide bolt catch over spacer.  Pre-drill holes using 3/32” bit.  Install screws.

Add felt bumper pad between door and library.

# Roof  Installation

Lay roof E upside down and position library (also upside down) on top, with most of the roof extending over the door.  Using pencil, mark outside of library on underside of roof.

Pre-drill 3/32” holes (2 on each side, 3 for front and back).  Important:  The front and back holes must be drilled at an angle to match angle of library front and back.

Return library to upside right position and center roof to match previously drawn lines.  Pre-drill side holes first using 3/32” bit.  Install trim screws.  Pre-drill front and back holes, being sure that drill is in vertical position.  Install trim screws.  (10 total)

# Shingle Installation

Cut shingles to ~27.5” to allow for ~¼” overhang.  Will require 4 rows.  Remove protective film from bottom row and position allowing for ~¼” overhang at back of library roof.  Press down shingle securely.  Secure top edge of shingle using staple gun with ⅜” staples.  Repeat for rows 3, 2 and 1.  Top row shingle should also overhang (front of roof) by ~¼”.  Ends of shingles (on sides of roof) may be curled up.  If so, they can also be secured with ⅜” staples.

# Medallion & Registration Plaque Installation

Center medallion on right side G of library and secure with the two screws.

Center Little Free Library registry plaque above door and secure with provided screws.

# Pole Assembly

Center pole H in middle of base K and mark outline of pole.  Pre-drill two holes using 5/32” bit.

Position base on pole and pre-drill holes using ⅛” bit.  Install two 3½” screws.

Position braces J on each side and pre-drill holes (through braces only) using 5/32“ bit.  Pre-drill holes (into base and pole) using ⅛” bit.  Make sure pole is perpendicular to base.  Install eight 3½” screws.

# Pole Installation

Dig 12” diameter hole, 18” to 24” deep.  Goal is to have library at chest height.  Can trim base of pole if needed.  Set pole in hole and hold vertical (using post level).  Mix one bag of cement and add around post, being sure to remove air bubbles.  Depending on final diameter of dug hole, a second bag of cement may be required.  Let cement harden.

# Library Installation

Center library over base and pre-drill holes through floor into base using ⅛” bit.  Install four 2½“ screws.